## Slide 1: Lecture: Pixels and Filters
Juan Carlos Niebles and Ranjay Krishna
Stanford Vision Lab

## Slide 2: Announcements
HW1 due Monday
HW2 is out
Class notes – Make sure to find the source and cite the images you use.

## Slide 3: What we will learn today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Some background reading:
Forsyth and Ponce, Computer Vision, Chapter 7

## Slide 4: What we will learn today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Some background reading:
Forsyth and Ponce, Computer Vision, Chapter 7

## Slide 5: Types of Images

## Slide 6: Types of Images

## Slide 7: Types of Images

## Slide 8: Binary image representation
Slide credit: Ulas Bagci

## Slide 9: Grayscale image representation
Slide credit: Ulas Bagci

## Slide 10: Color Image - one channel
Slide credit: Ulas Bagci

## Slide 11: Color image representation
Slide credit: Ulas Bagci

## Slide 12: Images are sampled
What happens when we zoom into the images we capture?

## Slide 13: Errors due Sampling
Slide credit: Ulas Bagci

## Slide 14: Resolution
is a sampling parameter, defined in dots per inch (DPI) or equivalent measures of spatial pixel density, and its standard value for recent screen technologies is 72 dpi
Slide credit: Ulas Bagci

## Slide 15: Images are Sampled and Quantized
An image contains discrete number of pixels
  A simple example
  Pixel value:
    “grayscale”
    (or “intensity”): [0,255]
231
75
148
Notes: Last time: Images as Matrices
intensity
temperature
depth

## Slide 16: Images are Sampled and Quantized
An image contains discrete number of pixels
  A simple example
  Pixel value:
    “grayscale”
    (or “intensity”): [0,255]
    “color”
      RGB: [R, G, B]
      Lab: [L, a, b]
      HSV: [H, S, V]
[249, 215, 203]
[90, 0, 53]
[213, 60, 67]

## Slide 17: With this loss of information (from sampling and quantization), Can we still use images for useful tasks?

## Slide 18: What we will learn today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Some background reading:
Forsyth and Ponce, Computer Vision, Chapter 7

## Slide 19: Histogram
Histogram of an image provides the frequency of the brightness (intensity) value in the image.
def histogram(im):
h = np.zeros(255)
for row in im.shape[0]:
for col in im.shape[1]:
val = im[row, col]
h[val] += 1

## Slide 20: Histogram
Histogram captures the distribution of gray levels in the image.
How frequently each gray level occurs in the image

## Slide 21: Histogram
Slide credit: Dr. Mubarak Shah

## Slide 22: Histogram – use case
Slide credit: Dr. Mubarak Shah

## Slide 23: Histogram – another use case
Slide credit: Dr. Mubarak Shah

## Slide 24: What we will learn today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Some background reading:
Forsyth and Ponce, Computer Vision, Chapter 7

## Slide 25: Images as discrete functions
Images are usually digital (discrete):
  Sample the 2D space on a regular grid
Represented as a matrix of integer values
pixel

## Slide 26: Images as coordinates
Cartesian coordinates
Notation for
discrete
functions

## Slide 27: Images as functions
An Image as a function f from R2 to RM:
  f( x, y ) gives the intensity at position ( x, y )
  Defined over a rectangle, with a finite range:
    f: [a,b] x [c,d ]  [0,255]
Domain
support
range

## Slide 28: Images as functions
An Image as a function f from R2 to RM:
  f( x, y ) gives the intensity at position ( x, y )
  Defined over a rectangle, with a finite range:
    f: [a,b] x [c,d ]  [0,255]
A color image:
Domain
support
range
Notes: Each r, g, b are functions that like the one above

## Slide 29: Histograms are a type of image function

## Slide 30: What we will learn today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Some background reading:
Forsyth and Ponce, Computer Vision, Chapter 7

## Slide 31: Systems and Filters
Filtering:
  Forming a new image whose pixel values are transformed from original pixel values
Goals:
Goal is to extract useful information from images, or transform images into another domain where we can modify/enhance image properties
  Features (edges, corners, blobs…)
  super-resolution; in-painting; de-noising

## Slide 32: System and Filters
we define a system as a unit that converts an input function f[n,m] into an output (or response) function g[n,m], where (n,m) are the independent variables.
  In the case for images, (n,m) represents the spatial position in the image.

## Slide 33
Super-resolution
De-noising
In-painting
Bertamio et al

## Slide 34: Images as coordinates
Cartesian coordinates
Notation for
discrete
functions

## Slide 35: 2D discrete-space systems (filters)
S is the system operator, defined as a mapping or assignment of a member of the set of possible outputs g[n,m] to each member of the set of possible inputs f[n,m].

## Slide 36: Filter example #1: Moving Average
2D DS moving average over a 3 × 3 window of neighborhood
1
1
1
1
1
1
1
1
1
h
Notes: Board:
Input image
Output image
each pixel results from a neighborhood operation

## Slide 37: Filter example #1: Moving Average
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Courtesy of S. Seitz

## Slide 38: Filter example #1: Moving Average
38
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 39: Filter example #1: Moving Average
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 40: Filter example #1: Moving Average
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 41: Filter example #1: Moving Average
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 42: Filter example #1: Moving Average
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 
Source: S. Seitz
Notes: What is the effect on the output?
What happens to the sharp edges?

## Slide 43: Filter example #1: Moving Average
In summary:
This filter “Replaces” each pixel with an average of its neighborhood.
Achieve smoothing effect (remove sharp features)
1
1
1
1
1
1
1
1
1

## Slide 44: Filter example #1: Moving Average

## Slide 45: Filter example #2: Image Segmentation
Image segmentation based on a simple threshold:
255,

## Slide 46: Properties of systems
Amplitude properties:
  Additivity

## Slide 47: Properties of systems
Amplitude properties:
  Additivity
  Homogeneity

## Slide 48: Properties of systems
Amplitude properties:
  Additivity
  Homogeneity
  Superposition

## Slide 49: Properties of systems
Amplitude properties:
  Additivity
  Homogeneity
  Superposition
  Stability

## Slide 50: Properties of systems
Amplitude properties:
  Additivity
  Homogeneity
  Superposition
  Stability
  Invertibility

## Slide 51: Properties of systems
Spatial properties
  Causality
  Shift invariance:

## Slide 52: Is the moving average system is shift invariant?
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 

## Slide 53: Is the moving average system is shift invariant?
Yes!

## Slide 54: Is the moving average system is casual?
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 

## Slide 55: Linear Systems (filters)
Linear filtering:
  Form a new image whose pixels are a weighted sum of original pixel values
  Use the same set of weights at each point
S is a linear system (function) iff it S satisfies
superposition property
Notes: Moving average is an example of a linear filter.
Here a more general definition.

## Slide 56: Linear Systems (filters)
Is the moving average a linear system?
Is thresholding a linear system?
  f1[n,m] + f2[n,m] > T
  f1[n,m] < T
  f2[n,m]<T
No!
Notes: Show on the board equations for moving average.

## Slide 57: 2D impulse function
1 at [0,0].
0 everywhere else

## Slide 58: LSI (linear shift invariant) systems
Impulse response
Notes: LSI systems can be characterized by the impulse response.
\delta_2 is the impulse (an image with 1 pixel =1, all the rest =0)
h is the response

## Slide 59: LSI (linear shift invariant) systems
1
1
1
1
1
1
1
1
1
h
Example: impulse response of the 3 by 3 moving average filter:

## Slide 60: Filter example #1: Moving Average
2D DS moving average over a 3 × 3 window of neighborhood
1
1
1
1
1
1
1
1
1
h
Notes: Board:
Input image
Output image
each pixel results from a neighborhood operation

## Slide 61: LSI (linear shift invariant) systems
A simple LSI is one that shifts the pixels of an image:
shifting property of the delta function
Notes: We can write any function as a sum of impulses…
Let’s pass this function over our system..
Using superposition, we get a sum over the impulse responses…
Final equation: we call this a convolution. Applying the impulse response h to f at all locations.

## Slide 62: LSI (linear shift invariant) systems
A simple LSI is one that shifts the pixels of an image:
Remember the superposition property:
shifting property of the delta function
superposition property
Notes: We can write any function as a sum of impulses…
Let’s pass this function over our system..
Using superposition, we get a sum over the impulse responses…
Final equation: we call this a convolution. Applying the impulse response h to f at all locations.

## Slide 63: LSI (linear shift invariant) systems
With the superposition property, any LSI system can be represented as a weighted sum of such shifting systems:
Notes: We can write any function as a sum of impulses…
Let’s pass this function over our system..
Using superposition, we get a sum over the impulse responses…
Final equation: we call this a convolution. Applying the impulse response h to f at all locations.

## Slide 64: LSI (linear shift invariant) systems
Rewriting the above summation:
Notes: We can write any function as a sum of impulses…
Let’s pass this function over our system..
Using superposition, we get a sum over the impulse responses…
Final equation: we call this a convolution. Applying the impulse response h to f at all locations.

## Slide 65: LSI (linear shift invariant) systems
We define the filter of a LSI as:
Notes: We can write any function as a sum of impulses…
Let’s pass this function over our system..
Using superposition, we get a sum over the impulse responses…
Final equation: we call this a convolution. Applying the impulse response h to f at all locations.

## Slide 66: What we will learn today?
Images as functions
Linear systems (filters)
Convolution and correlation
Some background reading:
Forsyth and Ponce, Computer Vision, Chapter 7

## Slide 67: 1D Discrete convolution (symbol: )
We are going to convolve a function f with a filter h.
h[k,l]
f[k,l]

## Slide 68: 1D Discrete convolution (symbol: )
We are going to convolve a function f with a filter h.
We first need to calculate h[n-k, m-l]
h[k]
h[-k]
h[n-k]

## Slide 69: Discrete convolution (symbol: )
We are going to convolve a function f with a filter h.
f[k]
h[-2-k]
g[-2]

## Slide 70: Discrete convolution (symbol: )
We are going to convolve a function f with a filter h.
f[k]
h[-1-k]
g[-1]

## Slide 71: Discrete convolution (symbol: )
We are going to convolve a function f with a filter h.
f[k]
h[-k]
g[0]

## Slide 72: Discrete convolution (symbol: )
We are going to convolve a function f with a filter h.
f[k]
h[1-k]
g[1]

## Slide 73: Discrete convolution (symbol: )
We are going to convolve a function f with a filter h.
f[k]
h[2-k]
g[2]

## Slide 74: Discrete convolution (symbol: )
We are going to convolve a function f with a filter h.
f[k]
h[n-k]
g[n]

## Slide 75: Discrete convolution (symbol: )
In summary, the steps for discrete convolution are:
Fold h[k,l] about origin to form h[−k]
Shift the folded results by n to form h[n − k]
Multiply h[n − k] by f[k]
Sum over all k
Repeat for every n
n

## Slide 76: 2D convolution
2D convolution is very similar to 1D.
The main difference is that we now have to iterate over 2 axis instead of 1.
n
Assume we have a filter(h[,]) that is 3x3. and an image (f[,]) that is 7x7.

## Slide 77: 2D convolution
2D convolution is very similar to 1D.
The main difference is that we now have to iterate over 2 axis instead of 1.
n
Assume we have a filter(h[,]) that is 3x3. and an image (f[,]) that is 7x7.

## Slide 78: 2D convolution
2D convolution is very similar to 1D.
The main difference is that we now have to iterate over 2 axis instead of 1.
n
Assume we have a filter(h[,]) that is 3x3. and an image (f[,]) that is 7x7.

## Slide 79: 2D convolution
2D convolution is very similar to 1D.
The main difference is that we now have to iterate over 2 axis instead of 1.
n
Assume we have a filter(h[,]) that is 3x3. and an image (f[,]) that is 7x7.

## Slide 80: 2D convolution
2D convolution is very similar to 1D.
The main difference is that we now have to iterate over 2 axis instead of 1.
n
Assume we have a filter(h[,]) that is 3x3. and an image (f[,]) that is 7x7.

## Slide 81: 2D convolution
2D convolution is very similar to 1D.
The main difference is that we now have to iterate over 2 axis instead of 1.
Assume we have a filter(h[,]) that is 3x3. and an image (f[,]) that is 7x7.

## Slide 82: LSI (linear shift invariant) systems
An LSI system is completely specified by its impulse response.
superposition
shifting property of the delta function
Discrete convolution
Notes: We can write any function as a sum of impulses…
Let’s pass this function over our system..
Using superposition, we get a sum over the impulse responses…
Final equation: we call this a convolution. Applying the impulse response h to f at all locations.

## Slide 83: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 84: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 85: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 86: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 87: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 88: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 89: 2D convolution example
Slide credit: Song Ho Ahn

## Slide 90: Convolution in 2D - examples
0
0
0
0
1
0
0
0
0
Original
?
=
Courtesy of D Lowe
*

## Slide 91: Convolution in 2D - examples
0
0
0
0
1
0
0
0
0
Original
Filtered
(no change)
=
Courtesy of D Lowe
*

## Slide 92: Convolution in 2D - examples
0
0
0
1
0
0
0
0
0
Original
?
=
Courtesy of D Lowe
*

## Slide 93: Convolution in 2D - examples
0
0
0
1
0
0
0
0
0
Shifted right
By 1 pixel
=
Courtesy of D Lowe
Original
*

## Slide 94: Convolution in 2D - examples
?
1
1
1
1
1
1
1
1
1
=
Courtesy of D Lowe
Original
*

## Slide 95: Convolution in 2D - examples
1
1
1
1
1
1
1
1
1
Blur (with a
box filter)
=
Courtesy of D Lowe
Original
*

## Slide 96: Convolution in 2D - examples
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
= ?
(Note that filter sums to 1)
1
1
1
1
1
1
1
1
1
0
0
0
0
1
0
0
0
0
-
0
0
0
0
1
0
0
0
0
+
“details of the image”
Courtesy of D Lowe
Original
Notes: Original image – blur = details!

## Slide 97
What does blurring take away?
original
smoothed (5x5)
–
detail
=
sharpened
=
Let’s add it back:
original
detail
+ a

## Slide 98: Convolution in 2D – Sharpening filter
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter: Accentuates differences with local average
=
Courtesy of D Lowe
Original

## Slide 99: Image support and edge effect
A computer will only convolve finite support signals.
  That is: images that are zero for n,m outside some rectangular region
numpy’s convolution performs 2D DS convolution of finite-support signals.
N1 ×M1
N2 ×M2
(N1 + N2 − 1) × (M1 +M2 − 1)
*
=

## Slide 100: Image support and edge effect
A computer will only convolve finite support signals.
What happens at the edge?
f
h
• zero “padding”
• edge value replication
• mirror extension
• more (beyond the scope of this class)
-> Matlab conv2 uses zero-padding

## Slide 101
Slide credit: Wolfram Alpha

## Slide 102: What we will learn today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation
Some background reading:
Forsyth and Ponce, Computer Vision, Chapter 7

## Slide 103: (Cross) correlation (symbol: )
Cross correlation of two 2D signals f[n,m] and g[n,m]
Equivalent to a convolution without the flip
(k, l) is called the lag
(g* is defined as the complex conjugate of g. In this class, g(n,m) are real numbers, hence g*=g.)
Notes: Equation is about the same.
Difference is with the complex conjugate)

## Slide 104: (Cross) correlation – example
Courtesy of J. Fessler
Notes: Use: compare similarity between “kernel” and image.

## Slide 105: (Cross) correlation – example
Courtesy of J. Fessler
Notes: Use: compare similarity between “kernel” and image.

## Slide 106: (Cross) correlation – example
numpy’s correlate
Courtesy of J. Fessler
Notes: Use: compare similarity between “kernel” and image.

## Slide 107
(Cross) correlation – example
Left
Right
scanline
Norm. cross corr. score

## Slide 108
Convolution vs. (Cross) Correlation
f*h
f**h

## Slide 109
Figure from “Computer Vision for Interactive Computer Graphics,” W.Freeman et al, IEEE Computer Graphics and Applications, 1998 copyright 1998, IEEE
Cross Correlation Application: Vision system for TV remote control
  - uses template matching
Notes: This is a figure from the book, figure 7.16. Read the caption for the story!

## Slide 110: properties
• Associative property:
• Distributive property:
The order doesn’t matter!

## Slide 111: properties
• Shift property:
• Shift-invariance:

## Slide 112: Convolution vs. (Cross) Correlation
A convolution is an integral that expresses the amount of overlap of one function as it is shifted over another function.
  convolution is a filtering operation
Correlation compares the similarity of two sets of data. Correlation computes a measure of similarity of two input signals as they are shifted by one another. The correlation result reaches a maximum at the time when the two signals match best .
  correlation is a measure of relatedness of two signals

## Slide 113: What we have learned today?
Image sampling and quantization
Image histograms
Images as functions
Linear systems (filters)
Convolution and correlation